## Slide 1
STRUCTURAL ENGINEERING LAB REPORT
Analysis of Truss Structures
Manual Calculation vs ANSYS Simulation Approach
Frais Asghar School of Mechanical & Manufacturing Engineering (SMME) National University of Sciences & Technology (NUST) May 2025

## Slide 2
Project Overview
What this lab set out to do, and how it was verified
1
Design
Built a 2D truss with 4 joints (A, B, C, D) and 5 members, supported by a roller at A and a pin at C.
2
Solve
Applied the Method of Joints to compute reaction forces and internal member forces under a 300 N horizontal load.
3
Verify
Rebuilt the same truss in ANSYS Workbench and compared simulated axial forces against hand calculations.
Result: Manual calculations and ANSYS simulation matched almost exactly (max axial force 212.13 N in both), confirming the accuracy of the analysis.
Frais Asghar | NUST · SMME
2

## Slide 3
Truss Theory & Assumptions
Foundational concepts behind the analysis
A truss is a rigid structure built from straight members pinned together at joints, used in bridges, roofs, and towers to carry loads efficiently. The Method of Joints analyzes equilibrium (ΣFx = 0, ΣFy = 0) at every joint to find each member's internal force.
1
All members are connected by frictionless pins at their ends
2
Loads are applied only at the joints
3
Members carry axial forces only — tension or compression
4
Self-weight of members is negligible vs. applied loads
Frais Asghar | NUST · SMME
3

## Slide 4
Truss Geometry & Applied Load
Roller support at A · Pin support at C · Horizontal load at D
AB
BC
AD
CD
BD
A
B
C
D
300 N
4 m
4 m
4 m
Load Derivation
Applied load is based on the last two digits of Qasim's CMS ID. CMS digits used: 30 Load = 30 × 10
Load = 300 N (Horizontal, at Joint D)
Supports A — Roller (vertical reaction only) C — Pin (horizontal + vertical reaction)
Frais Asghar | NUST · SMME
4

## Slide 5
Analysis Roadmap
From free-body diagram to simulation-verified results
01
Identify Structure
Joints, members, supports & applied load
02
Whole-Truss Equilibrium
ΣFx, ΣM, ΣFy → reaction forces
03
Method of Joints
Solve joint A → B → C for member forces
04
Tabulate & Plot
Compile reactions & internal forces
05
ANSYS Verification
Simulate and compare against hand calc
Frais Asghar | NUST · SMME
5

## Slide 6
External Reaction Forces
Whole-truss equilibrium equations
ΣFx = 0
300 − RCx = 0 → RCx = 300 N (leftward)
ΣM_C = 0
(RAy)(8) + (300)(4) = 0 → RAy = −150 N (150 N downward)
ΣFy = 0
RAy + RCy = 0 → RCy = 150 N (upward)
R_Ay
150 N
Downward
R_Cx
300 N
Leftward
R_Cy
150 N
Upward
Frais Asghar | NUST · SMME
6

## Slide 7
Internal Forces. Method of Joints
Solved sequentially: Joint A → Joint B → Joint C
A
Joint A
Vertical: FAD sin45° − 150 = 0 → FAD = 212.13 N (Tension)
Horizontal: FAB + FAD cos45° = 0 → FAB = −150 N (Compression)
B
Joint B
Horizontal: FBC − FAB = 0 → FBC = 150 N (Tension)
Vertical: FBD = 0 N → Zero-force member
C
Joint C
Horizontal: −FBC + FCD cos45° + RCx = 0 → FCD = −212.13 N (Compression)
Frais Asghar | NUST · SMME
7

## Slide 8
Complete Force Summary
Reactions and member forces from the method of joints
Quantity | R_Ay | R_Cx | R_Cy | F_AB | F_AD | F_BC | F_BD | F_CD
Value (N) | 150 | 300 | 150 | 150 | 212.13 | 150 | 0 | 212.13
Nature | Downward | Leftward | Upward | Compression | Tension | Tension | Zero-force | Compression
Members in Tension: AD (212.13 N), BC (150 N) Members in Compression: AB (150 N), CD (212.13 N) Zero-Force Member: BD (0 N)
Maximum internal force: 212.13 N (members AD & CD) — this governs member sizing and matches the ANSYS peak exactly.
Frais Asghar | NUST · SMME
8

## Slide 9
Force Magnitudes at a Glance
External reactions vs. internal member forces
External Forces (N)
Chart: 
| R_Ay | R_Cx | R_Cy
External Forces | 150 | 300 | 150
Internal Member Forces (N)
Chart: 
| F_AB | F_AD | F_BC | F_BD | F_CD
Internal Forces | 150 | 212.13 | 150 | 0 | 212.13
Frais Asghar | NUST · SMME
9

## Slide 10
ANSYS Workbench Verification
Simulated axial force distribution vs. hand calculation
(Colors mirror the ANSYS axial-force contour legend)
212.13 Max
0.00 (BD)
−212.13 Min
Max Axial Force
Manual: 212.13 N (AD, Tension) ANSYS: 212.13 N
Min Axial Force
Manual: −212.13 N (CD, Compression) ANSYS: −212.13 N
Zero-Force Member
Manual: BD = 0 N ANSYS: BD ≈ 0 N (green)
Frais Asghar | NUST · SMME
10

## Slide 11
Discussion & Conclusion
Key Findings
• Reactions: R_Ay = 150 N (down), R_Cy = 150 N (up), R_Cx = 300 N (left)
• Tension members: AD = 212.13 N, BC = 150 N
• Compression members: AB = 150 N, CD = 212.13 N
• BD is a zero-force member under this loading
• ANSYS confirmed max/min axial forces of ±212.13 N, matching hand calculations exactly
Conclusion
The truss was analyzed for internal member forces and support reactions using the Method of Joints, then verified through ANSYS simulation. Both approaches produced matching values, confirming the analysis was correct and demonstrating a practical link between classical statics and finite element verification.
References
1. Hibbeler, R. C. Engineering Mechanics: Statics, 14th Ed., Pearson, 2016.
2. ANSYS Workbench Documentation, 2025.
Frais Asghar | NUST · SMME
11